## Slide 1: Chapter 5 Low Noise Amplifiers
5.1 General Considerations
5.2 Problem of Input Matching
5.3 LNA Topologies
5.4 Gain Switching
5.5 Band Switching
5.6 High IP2 LNAs
5.7 Nonlinearity Calculations
Behzad Razavi, RF Microelectronics.
Prepared by Bo Wen, UCLA

## Slide 2: Chapter Outline
Basic LNA Topologies
Alternative LNA
Topologies
Nonlinearity of LNAs
CS Stage with Inductive Load
CS Stage with Resistive Feedback
CG Stage
CS Stage with Inductive Degeneration
Variants of CS LNA
Noise-Cancelling LNAs
Differential LNAs
Nonlinearity Calculations
Differential and Quasi-Differential LNAs

## Slide 3: General Considerations: Noise Figure
The noise figure of the LNA directly adds to that of the receiver.
It is expected that the LNA contributes 2 to 3 dB of noise figure. Consider the simple example shown below:
A noise figure of 2 dB with respect to a source impedance of 50Ω translates to:
an extremely low value.

## Slide 4
Example of Metal Resistance and Noise Figure
A student lays out an LNA and connects its input to a pad through a metal line 200 μm long. In order to minimize the input capacitance, the student chooses a width of 0.5 μm for the line. Assuming a noise figure of 2 dB for the LNA and a sheet resistance of 40 mΩ/ □ for the metal line, determine the overall noise figure. Neglect the input-referred noise current of the LNA.
We draw the equivalent circuit as shown in figure below, pretending that the line resistance, RL, is part of the LNA. The total input-referred noise voltage of the circuit inside the box is therefore equal to V n,in2+4kTRL. We thus write
where NFLNA denotes the noise figure of the LNA without the line resistance. Since NFLNA = 2 dB ≡ 1.58 and RL = (200/0.5) × 40 mΩ/□ = 16 Ω, we have

## Slide 5: General Considerations: Gain
The gain of the LNA must be large enough to minimize the noise contribution of subsequent stages, specifically, the downconversion mixer(s).
The noise and IP3 of the stage following the LNA are divided by different LNA gains. Assuming a unity voltage gain for the mixer for simplicity, The overall noise figure is thus equal to
In figure above (right),

## Slide 6: General Considerations: Input Return Loss
The quality of the input match is expressed by the input “return loss,” defined as the reflected power divided by the incident power. For a source impedance of RS, the return loss is given by:
Figure above plots contours of constant Γ in the Zin plane. Each contour is a circle with its center shown.

## Slide 7: General Considerations: Stability
A parameter often used to characterize the stability of circuits is the “Stern stability factor,” defined as:
A cascade stage exhibits a high reverse isolation, i.e., S12 ≈ 0. If the output impedance is relatively high so that S22 ≈ 1, determine the stability conditions.
With S12 ≈ 0 and S22 ≈ 1,
and hence
In other words, the forward gain must not exceed a certain value. For Δ < 1, we have
concluding that the input resistance must remain positive.

## Slide 8: General Considerations: Linearity
In most applications, the LNA does not limit the linearity of the receiver.
An exception to the above rule arises in “full-duplex” systems:
Leakages through the filter and the package yield a finite isolation between ports 2 and 3 as characterized by an S32 of about -50 dB. The received signal may be overwhelmed.

## Slide 9: General Considerations: Bandwidth
An 802.11a LNA must achieve a -3-dB bandwidth from 5 GHz to 6 GHz. If the LNA incorporates a second-order LC tank as its load, what is the maximum allowable tank Q?
As illustrated in figure below, the fractional bandwidth of an LC tank is equal to Δω/ω0 = 1/Q. Thus, the Q of the tank must remain less than 5.5 GHz/1 GHz = 5.5.
The LNA must provide a relatively flat response for the frequency range of interest, preferably with less than 1 dB of gain variation. The LNA -3-dB bandwidth must therefore be substantially larger than the actual band so that the roll-off at the edges remains below 1 dB.

## Slide 10: Band Switching
LNA designs that must achieve a relatively large fractional bandwidth may employ a mechanism to switch the center frequency of operation.
As depicted below, an additional capacitor, C2, can be switched into the tank, thereby changing the center frequency

## Slide 11: Problem of Input Matching: Input Admittance of a CS Stage
LNAs are typically designed to provide a 50-W input resistance and negligible input reactance. This requirement limits the choice of LNA topologies.
The real and imaginary parts of the input admittance are, respectively, equal to:
Why did we compute the input admittance rather than the input impedance for the circuit of figure above.
The choice of one over that other is somewhat arbitrary. In some circuits, it is simpler to compute Yin. Also, if the input capacitance is cancelled by a parallel inductor, then Im{Yin} is more relevant. Similarly, a series inductor would cancel Im{Zin}. We return to these concepts later in this chapter.

## Slide 12: Resistive Termination for Matching
express the total output noise as:
Such a topology is designed in three steps:
(1) M1 and RD provide the required noise figure and gain
(2) RP is placed in parallel with the input to provide Re{Zin} = 50Ω
(3) an inductor is interposed between RS and the input to cancel Im{Zin}.
the noise figure is given by:

## Slide 13
Example of Input Matching by Transforming a Large Resistance Down (Ⅰ)
A student decides to defy the above observation by choosing a large RP and transforming its value down to RS. The resulting circuit is shown below (left), where C1 represents the input capacitance of M1. (The input resistance of M1 is neglected.) Can this topology achieve a noise figure less than 3 dB?
Consider the more general circuit in figure below (right), where H(s) represents a lossless network similar to L1 and C1. Since it is desired that Zin = RS, the power delivered by Vin to the input port of H(s) is equal to (Vin,rms/2)2/RS. This power must also be delivered to RP :
It follows that

## Slide 14
Example of Input Matching by Transforming a Large Resistance Down (Ⅱ)
Let us now compute the output noise with the aid of figure below (left). The output noise due to the noise of RS is readily obtained
How about the noise of RP? We must first determine the value of Rout. We draw the circuit as depicted above (middle) and recall that a passive reciprocal network exhibiting a real port impedance of RS also produces a thermal noise of 4kTRS. From the equivalent circuit shown above (right), we note that the noise power delivered to the RS on the left is equal to kT.

## Slide 15: LNA Topologies: Overview
Our preliminary studies thus far suggest that the noise figure, input matching, and gain constitute the principal targets in LNA design. We present a number of LNA topologies and analyze their behavior with respect to these targets.

## Slide 16: Common-Source Stage with Inductive Load
In general, the trade-off between the voltage gain and the supply voltage in the CS stage with resistive load makes it less attractive as the latter scales down with technology. For example, at low frequencies,
To circumvent the trade-off expressed above and also operate at higher frequencies,
the CS stage can incorporate an inductive load.
Can operate with very low supply voltages
L1 resonates with the total capacitance at the output node, affording a much higher operation frequency than does the resistively-loaded counterpart

## Slide 17: Input Matching of CS Stage with Inductive Load (Ⅰ)
We redraw the circuit as depicted above (right) the inductor loss is modeled by a series resistance, RS, The tank impedance is given by
Adding the voltage drop across CF to the tank voltage, we have

## Slide 18: Input Matching of CS Stage with Inductive Load (Ⅱ)
Substitution of ZT gives:
For s = jω:
Since the real part of a complex fraction (a+jb)/(c+jd) is equal to (ac+bd)/(c2 +d2), we have
It is thus possible to select the values so as to obtain Re{Zin} = 50Ω

## Slide 19: Neutralization of CF by LF
The feedback capacitance gives rise to a negative input resistance at other frequencies, potentially causing instability.
The numerator falls to zero at a frequency given by
Thus, at this frequency (if it exists), Re{Zin} changes sign
It is possible to “neutralize” the effect of CF in some frequency range through the use of parallel resonance.
Will introduce significant parasitic capacitances at the input and output and degrading the performance.
Notes: 通过使用并联谐振，有可能在某些频率范围内 "中和 "CF的影响。
将在输入和输出端引入大量的寄生电容，并使性能下降。

## Slide 20: Common-Source Stage with Resistive Feedback
If channel-length modulation is neglected, we have:
输入阻抗 这个模电书上有。
We must choose:
负载和源内阻相等， 匹配网络，放大效果最好。
In figure above (right):
电流* 电阻。 M2 产生的电阻比较大。
Notes: 假设输入电容不是domainate, gm = 1/50 = 0.02 ,在合理的范围内,
增益Av是可控的,

## Slide 21: Noise Figure of CS Stage with Resistive Feedback
The noise of RF appears at the output:
Mos管本身也有电阻，
gm1 * Rs =1
NF，
Notes: 非常适合先进工艺. 加了个电阻， 4kT Rf。
高频的时候, flick noise也没有了, gm Rs是上面的偏置, 1 是大家都在的, 希望Rf比较大, NF才会小,

## Slide 22
Example of NF and Transistor Overdrive Voltages
Express the fourth term on the right-hand side of Noise Figure calculated above in terms of transistor overdrive voltages.
Since gm = 2ID/(VGS - VTH), we write gm2RS = gm2/gm1 and
Solution:
That is, the fourth term becomes negligible only if the overdrive of the current source remains much higher than that of M1—a difficult condition to meet at low supply voltages because |VDS2| = VDD - VGS1. We should also remark that heavily velocity-saturated MOSFETs have a transconductance given by gm = ID/(VGS - VTH) and still satisfy equation above.也就是说，只有当电流源的过驱动一直远高于 M1 时，第四项才可以忽略不计——这是在低电源电压下难以满足的条件，因为 |VDS2| = VDD - VGS1。 我们还应该指出，重度速度饱和的 MOSFET 具有由 gm = ID/(VGS - VTH) 给出的跨导，并且仍然满足上述等式。
Notes: 需要看她的过驱动电压,

## Slide 23
Example of CS Stage with Active Load
In the circuit of figure below, the PMOS current source is converted to an “active load,” amplifying the input signal. The idea is that, if M2 amplifies the input in addition to injecting noise to the output, then the noise figure may be lower. Neglecting channel-length modulation, calculate the noise figure. (Current source I1 defines the bias current and C1 establishes an ac ground at the source of M2).
在下图电路中，PMOS 电流源被转换为“有源负载”，放大输入信号。 这个想法是，如果 M2 除了向输出注入噪声之外还放大输入，那么噪声系数可能会更低。 忽略通道长度调制，计算噪声系数。 （电流源 I1 定义偏置电流，C1 在 M2 的源极处建立交流接地）。
For small-signal operation, M1 and M2 appear in parallel, behaving as a single transistor with a transconductance of gm1 + gm2. Thus, for input matching, gm1 + gm2 = 1/RS. The noise figure is still given by previous equation, except that (gm1 + gm2)RS = γ. That is,
对于小信号操作，M1 和 M2 并联出现，表现为具有 gm1 + gm2 跨导的单个晶体管。 因此，对于输入匹配，gm1 + gm2 = 1/RS。 噪声系数仍然由前面的方程给出，除了 (gm1 + gm2)RS = γ。 那是，
This circuit is therefore superior, but it requires a supply voltage equal to VGS1 + |VGS2| + VI1, where VI1 denotes the voltage headroom necessary for I1.
Notes: 经常会采用对称的结构, 电路有电流源, 两个管子可以提供两个有效的gm, 这个放大器就很有优势.

## Slide 24: Common-Gate Stage
The voltage gain from X to the output node at the output resonance frequency is then equal to:
The low input impedance of the common-gate (CG) stage makes it attractive for LNA design.
And noise:

## Slide 25
Example of Noise in CG Stage with Different Biasing (Ⅰ)
We wish to provide the bias current of the CG stage by a current source or a resistor. Compare the additional noise in these two cases.
For a given Vb1 and VGS1, the source voltages of M1 in the two cases are equal and hence VDS2 is equal to the voltage drop across RB (=VRB). Operating in saturation, M2 requires that VDS2 ≥ VGS2 - VTH2. We express the noise current of M2 as (M2管子会带来噪声,好处是两个gm)
And that of RB as

## Slide 26
Example of Noise in CG Stage with Different Biasing (Ⅱ)
We wish to provide the bias current of the CG stage by a current source or a resistor. Compare the additional noise in these two cases.
Since VGS2-VTH2 ≤ VRB, the noise contribution of M2 is about twice that of RB (for γ ≈ 1). Additionally, M2 may introduce significant capacitance at the input node.
The use of a resistor is therefore preferable, so long as RB is much greater than RS so that it does not attenuate the input signal. Note that the input capacitance due to M1 may still be significant. We will return to this issue later. Figure 5.18 shows an example of proper biasing in this case.

## Slide 27
Example of Input Impedance of CG Stage
Neglecting the capacitances of M1 in figure above, plot the input impedance as a function of frequency.
At very low or very high frequencies, the tank assumes a low impedance, yielding Rin = 1/gm [or 1/(gm + gmb) if body effect is considered]. Figure below depicts the behavior.
Solution:

## Slide 28: More about Channel-Length Modulation
With the strong effect of R1 on Rin, we must equate the actual input resistance to RS to
guarantee input matching:
The voltage gain of the CG stage with a finite rO is expressed as
In summary, the input impedance of the CG stage is too low if channel-length modulation is neglected and too high if it is not.
In order to alleviate the above issue, the channel length of the transistor can be increased
If rO and R1 are comparable, then the voltage gain is on the order of gmrO=4, a very low value.

## Slide 29: Issues of Cascode CG Stage: Noise Contribution of M2
Neglecting the gate-source capacitance, channel-length modulation, and body effect of M2, we express the transfer function from Vn2 to the output at the resonance frequency as
The noise contribution of M2 is negligible for frequencies up to the zero frequency, (2rO1CX)-1, but begins to manifest itself thereafter.

## Slide 30
Computation of Gain with CGS2
Assuming 2rO1 >> |CXs|-1 at frequencies of interest so that the degeneration impedance in the source of M2 reduces to CX, recompute the above transfer function while taking CGS2 into account. Neglect the effect of rO2.
Writing a KVL in the input loop gives
At frequencies well below the fT of the transistor
That is, the noise of M2 reaches the output unattenuated if ω is much greater than (2rO1CX)-1

## Slide 31: Issues of Cascode CG Stage: Voltage Headroom Limitation
The two transistors M1 and M2 consume a voltage headroom of one VGS plus one overdrive (VGS1 -VTH1).
In order to avoid the noise-headroom trade-off imposed by RB, and also cancel the input capacitance of the circuit, CG stages often employ an inductor for the bias path.

## Slide 32: Cascode CS Stage with Inductive Degeneration: Input Impedance
The feedback through the gate-drain capacitance many be exploited to produce the required real part but it also leads to a negative resistance at lower frequencies.
We have: 选择良好的L1和Cgs1 可以抵消虚部.
Since VX = VGS1 + VP
Thus, the third term can be chosen equal to 50Ω. 没有电阻但是可以实现实部为电阻
In practice, the degeneration inductor is often realized as a bond wire with the reasoning that the latter is inevitable in packaging and must be incorporated in the design.
Notes: 电感放在M1下面, 就是degeneration退化, 如果这个地方放电阻, 电流分压了增益会变小, 高频的时候L和C会相互抵消, 会变成一个阻抗.

## Slide 33
Input Impedance of CS Stage in the Presence of CGD
Determine the input impedance of the circuit shown below (left) if CGD is not neglected and the drain is tied to a load resistance R1. Assume R1 ≈ 1/gm (as in a cascode).
From equivalent shown here
(right):
Solution:
Notes: 推导比较复杂, 大作业可以写这个公式

## Slide 34: NF Calculation (Ⅰ)
Excluding the effect of channel-length modulation, body effect, CGD and Cpad for simplicity
KVL around the input loop yields:
The coefficient of Iout represents the transconductance gain of the circuit:
Notes: 这里多了一个LG, 为什么?

## Slide 35: NF Calculation (Ⅱ)
Interestingly, the transconductance of the circuit remains independent of L1, LG, and gm so long as the input is matched
For gmL1/CGS1 = RS
We arrive at the noise figure of the circuit:
It is important to bear in mind that this result holds only at the input resonance frequency and if the input is matched.
Notes: w0是工作频率, wT是截止频率. 用这种电路可以做到非常低的噪声系数.
重要的是要记住，这个结果只在输入谐振频率和输入匹配的情况下成立。 射频对工艺的要求非常高.

## Slide 36: Cascode CS Stage with Inductive Degeneration
Add a cascode transistor in the output branch to suppress the effect of negative resistance.
The voltage gain:
The impedance seen at the source of M2,
RX rises sharply at the output resonance
frequency.
The voltage gain from the gate to the drain of M1:
Notes: 这个是重点, 可以认为M2 没有增益, 作为buffer.

## Slide 37: Design Procedure (Ⅰ)
The procedure begins with four knowns: the frequency of operation, ω0, the value of the degeneration inductance, L1, the input pad capacitance, Cpad, and the value of the input series inductance, LG.
Governing the design are the following equations:
In the next step, the dimensions of the cascode device are chosen equal to those of the input transistor.
The design procedure continues with selecting a value for LD such that it resonates at ω0 with the drain-bulk and drain-gate capacitances of M2, the input capacitance of the next stage, and the inductors’s own parasitic capacitance.

## Slide 38: Design Procedure (Ⅱ)
In the last step of the design, we must examine the input match. Due to the Miller multiplication of CGD1 , it is possible that the real and imaginary parts depart from their ideal values, necessitating some adjustment in LG.
Alternatively, the design procedure can begin with known values for NF and L1 and the following two equations:
The overall LNA appears as shown on right:

## Slide 39
Example of Choosing RB
How is the value of RB chosen in figure above?
Since RB appears in parallel with the signal path, its value must be maximized. Is RB = 10RS sufficiently high? As illustrated in figure below, the series combination of RS and LG can be transformed to a parallel combination with RP ≈ Q2RS ≈ (LGω0/RS)2RS. We note that a voltage gain of, say, 2 at the input requires Q = 3, yielding RP ≈ 450 Ω. Thus, RB = 10RS becomes comparable with RP , raising the noise figure and lowering the voltage gain. RB must remain much greater than RP .
Large resistors may suffer from significant parasitic capacitance. However, increasing the length of a resistor does not load the signal path anymore even though it leads to a larger overall parasitic capacitance.

## Slide 40
Comparison Between Input Matching Bandwidth for CG and CS Stage
It is believed that input matching holds across a wider bandwidth for the CG stage than for the inductively degenerated CS stage. Is this statement correct?
For the CS stage (left)
If the center frequency of interest is ω0
For the CG stage (right), on the other hand:
For ω << ωT

## Slide 41
Design Example of Cascode CS LNA (Ⅰ)
Design a cascode CS LNA for a center frequency of 5.5 GHz in 65-nm CMOS technology.
We begin with a degeneration inductance of 1 nH and the same input transistor as that in the CG stage in previous example. Interestingly, with a pad capacitance of 50 fF, the input resistance happens to be around 60Ω. (Without the pad capacitance, Re{Zin} is in the vicinity of 600 Ω.) We thus simply add enough inductance in series with the gate (LG = 12 nH) to null the reactive component at 5.5 GHz.
The design of the cascode device
and the output network is identical
to that of the CG example.

## Slide 42
Design Example of Cascode CS LNA (Ⅱ)
Figure below shows the simulated characteristics. We observe that the CS stage has a higher gain, a lower noise figure, and a narrower bandwidth than the CG stage in previous example.
Notes: 一开始增益做大,后面流片会减少,

## Slide 43: Variants of Common-Gate LNA: CG LNA with Feedback (Ⅰ)
If channel length modulation and body effect are neglected, the closed-loop input impedance is equal to:
At resonance,
To calculate noise figure, we first calculate the gain with the aid of the circuit on the left.
The block having a gain (or attenuation factor) of α senses the output voltage and subtracts a fraction thereof from the input.

## Slide 44: Variants of Common-Gate LNA: CG LNA with Feedback (Ⅱ)
For output noise calculation, we construct the circuit of figure on the right
The NF can be lowered by raising gm
Notes: 这个是这节课的重点, 热噪声gmmma, 要想怎么去除.

## Slide 45: CG LNA with Feedforward
The block having a gain (or attenuation factor) of α senses the output voltage and subtracts a fraction thereof from the input.
with the noise of the gain stage A:

## Slide 46: CG Stage with Transformer Feedforward
For a coupling factor of k between the primary and the secondary and a turns ratio of n, the transformer provides a voltage gain of kn.
On-chip transformer geometries make it difficult to achieve a voltage gain higher than roughly 3, even with stacked spirals

## Slide 47: Noise-Canceling LNAs: Basic Ideas
“Noise-canceling LNAs” aim to cancel the term representing the contribution of the input transistor in the noise figure of LNAs.
First identify two nodes at which the signal appears with opposite polarities but the noise of the input transistor appears with the same polarity.
Then their voltages can be properly scaled and summed such that the signal components add and the noise components cancel.

## Slide 48: Noise-Canceling LNAs: Noise Figure
The NF can be lowered by raising gm
We obtain the noise figure as:
Since A1 = 1 + RF/RS

## Slide 49: Noise-Canceling LNAs: Frequency-Dependent NF and Circuit Implementation
It can be proved that the frequency-dependent noise figure is expressed as
where NF(0) is given by equation in previous NF calculation and f0 = 1/(πRSCin)

## Slide 50
Example of an Alternative Implementation
Figure below shows an alternative implementation of a noise-canceling LNA that also performs single ended to differential conversion. Neglecting channel-length modulation, determine the condition for noise cancellation and derive the noise figure.
The circuit follows the noise cancellation principle because (a) the noise of M1, Vn1, sees a source follower path to node X and a common-source path to node Y , exhibiting opposite polarities at these two nodes, and (b) the signal sees a common-gate path through X and Y , exhibiting the same polarity. For noise cancellation, we must have
and, since gm1 = 1/RS

## Slide 51: Reactance-Cancelling LNAs
The idea is to exploit the inductive input impedance of a negative-feedback amplifier so as to cancel the input capacitance, Cin.
the input admittance is given by
At frequencies well below ω0, 1/Re{Y1} reduces to RF /(1+A0), which can be set equal to RS, and Im{Y1} is roughly -A0ω/(RF ω0), which can be chosen to cancel Cinω.

## Slide 52: Gain Switching in CG Stage
Choose the devices in the above circuit for a gain step of 3 dB.
we have
also
Solution:

## Slide 53: LNA Bypass
Receiver designs in which the LNA nonlinearity becomes problematic at high input levels can “bypass” the LNA in very-low-gain modes.
Notes: LNA 可能要把增益变成负数,如果要更大的动态范围.

## Slide 54: Band Switching
LNAs that must operate across a wide bandwidth or in different bands can incorporate band switching.
We prefer the implementation above (right), where S1 is formed as an NMOS device tied to ground.

## Slide 55: Band Switching by Programmable Cascode Branches
An alternative method of band switching incorporates two or more tanks
The principal drawback of this approach is the capacitance contributed by the additional cascode device(s) to node Y .
Also, the spiral inductors have large footprints, making the layout and routing more difficult.

## Slide 56: High-IP2 LNAs: Differential LNAs
Differential LNAs can achieve high IP2’s because, symmetric circuits produce no even-order distortion.
In principle, any of the single-ended LNAs studied thus far can be converted to differential
form. Shown above are CG (left) and CS (right) stages. 做成差分是解决IP2最简单的方法, 但是电感面积大,

## Slide 57: Use of Balun at RX Input
Since the antenna and the preselect filter are typically single-ended, a transformer must precede the LNA to perform single-ended to differential conversion.
The transformer is called a “balun,” an acronym for “balanced-to-unbalanced” conversion because it can also perform differential to single-ended conversion if its two ports are swapped.
Figure above (right) shows the setup for output noise calculation.

## Slide 58: Differential CG LNA: Noise Figure
Assuming it is designed such that the impedance seen between each input node and ground is equal to RS1/2
From the symmetry of the circuit that we can compute the output noise of each half circuit and add the output powers:

## Slide 59: Comparison of Single-Ended and Differential CG LNAs
Voltage gain of differential CG LNA is twice that of the single ended one. On the other hand, the overall differential circuit contains two R1’s at its output, each contributing a noise power of 4kTR1.

## Slide 60: Example of Differential Version and Noise Figure
An amplifier having a high input impedance employs a parallel resistor at the input to provide matching. Determine the noise figure of the circuit and its diff. version, shown below (middle), where two replicas of the amplifier are used.
Noise figure of the single-ended circuit:
For the differential version:

## Slide 61: Differential CS LNA
Recall that the input resistance of each half circuit is equal to L1ωT and must now be halved. This is accomplished by halving L1.
With input matching and a degeneration inductance of L1, the voltage gain was found to be R1/(2L1ω0), which is now doubled.
The differential CS LNA behaves differently from its CG counterpart.

## Slide 62: Differential CS LNA: Noise Figure
Neglecting the contribution of the cascode device, if the input is matched, half of the noise current of the input transistor flows from the output node.

## Slide 63: Comparison with the Noise Figure of the Original Single-Ended LNA
Compared with the Noise Figure of the Original Single-Ended LNA, both the transistor contribution and the load contribution are halved.
However, this result holds only if the design can employ tow degeneration inductors, each having half the value of that in the single-ended counterpart.

## Slide 64: Differential CS Stage with On-Chip Degeneration Inductors
The NF advantage implied previously may not materialize in reality because the loss of the balun is not negligible.
The design can incorporate on-chip degeneration inductors while converting the effect of the (inevitable) bond wire to a common-mode inductance.

## Slide 65: Singe-Ended to Differential Conversion
At low to moderate frequencies, VX and VY are differential and the voltage gain is equal to gm1,2RD.
At high frequencies, however, two effects degrade the balance of the phases: the parasitic capacitance at node P and the gate-drain capacitance of M1
The capacitance at P can be nulled through the use of a parallel inductor, but the CGD1 feedforward persists.

## Slide 66: Example of Choice of LP
A student computes CP in previous figure as CSB1 + CSB2 + CGS2, and selects the value of LP accordingly. Is this an appropriate choice?
No, it is not. For LP to null the phase shift at P, it must resonate with only CSB1+CSB2. This point can be seen by examining the voltage division at node P. As shown below, in the absence of CSB1 + CSB2,
For VP to be exactly equal to half of Vin (with zero phase difference), we must have Z1 = Z2. Since each impedance is equal to (gm + gmb)-1||(CGSs)-1, we conclude that CGS2 must not be nulled.
Solution:

## Slide 67: Use of On-Chip Inductors for Resonance and Degeneration
The topology discussed above still does not provide input matching. We must therefore insert (on-chip) inductances in series with the sources of M1 and M2.
Here, LP1 and LP2 resonate with CP1 and CP2, respectively, and LS1+LS2 provides the necessary input resistance.

## Slide 68: Balun Issues
External baluns with a low loss (e.g., 0.5 dB) in the gigahertz range are available from manufacturers, but they consume board space and raise the cost.
Integrated baluns, on the other hand, suffer from a relatively high loss and large capacitances.
The resistance and capacitance associated with the spirals and the sub-unity coupling factor make such baluns less attractive.

## Slide 69: Use of 1-to-N Balun in an LNA
A student attempts to use a 1-to-N balun with a differential CS stage so as to amplify the input voltage by a factor of N and potentially achieve a lower noise figure. Compute the noise figure in this case.
Since still half of the noise current of each input transistor flows to the output node, the noise power measured at each output is given by
The gain from Vin to the differential output is now equal to NR1/(2L1ω0). Doubling the above power, dividing by the square of the gain, and normalizing to 4kTRS, we have
We note, with great distress, that the first two terms have risen by a factor of N2

## Slide 70: Realization of Baluns with Non-Unity Turns Ratio
On-chip baluns with a non-unity turns ratio are difficult to design and suffer from a higher loss and a lower coupling factor.
Stacked Spirals Embedded Spirals

## Slide 71: Other Methods of IP2 Improvement
A possible approach to raising the IP2 entails simply filtering the low-frequency second-order intermodulation product, called the beat component
With this substantial suppression, the IP2 of the LNA is unlikely to limit the RX performance, calling for techniques that improve the IP2 of mixers.

## Slide 72: Nonlinearity Calculations
Systems with weak static nonlinearity can be approximated by a polynomial such as y = α1x + α2x2 + α3x3. Let us devise a method for computing α1-α3 for a given circuit. In many circuits, it is difficult to derive y as an explicit function of x. However, we recognize that
It is important to note that in most cases, x = 0 in fact corresponds to the bias point of the circuit with no input perturbation.

## Slide 73: Degenerated CS Stage-IP3 Calculation (Ⅰ)
For a simple square-law device
Since VGS = Vin - RSID,
Hence
Also
线性度和
Thus, in the absence of signals

## Slide 74: Degenerated CS Stage-IP3 Calculation (Ⅱ)
We now compute the second derivative
With no signals
Lastly, we determine the third derivative
Which reduces to
To compute the IP3 of the stage, we write

## Slide 75: CS Stage Driven by Finite Signal Source Impedance
A student measures the IP3 of the CS stage discussed above in the laboratory and obtains a value equal to half of that predicted by above equation. Explain why.
The test setup is shown above, where the signal generator produces the required input. The discrepancy arises because the generator contains an internal output resistance RG = 50 Ω, and it assumes that the circuit under test provides input matching, i.e., Zin = 50 Ω. The generator’s display therefore shows A0/2 for the peak amplitude. The simple CS stage, on the other hand, exhibits a high input impedance, sensing a peak amplitude of A0 rather than A0/2. Thus, the level that the student reads is half of that applied to the circuit. This confusion arises in IP3 measurements because this quantity has been traditionally defined in terms of the available input power.
Solution:

## Slide 76: Example of IP3 Calculation of a CG Stage
Compute the IP3 of a common-gate stage if the input is matched. Neglect channel-length modulation and body effect.
Differentiating both sides with respect to Vin gives:
In the absence of signals
The second derivative is identical to that of the CS stage
and the third derivative emerges as

## Slide 77: Undegenerated CS Stage: IP3 Calculation (Ⅰ)
The effect of mobility degradation due to both vertical and lateral fields in the channel can be approximated as:
And
Replace VGS with Vin + VGS0, obtaining
It follows that

## Slide 78: Undegenerated CS Stage: IP3 Calculation (Ⅱ)
We note that the IP3 rises with the bias overdrive voltage, reaching a maximum of

## Slide 79: Calculation with Another Approximation
If the second term in the denominator of previous approximation of ID is only somewhat less than unity, a better approximation must be used, e.g., (1 + ε)-1 ≈ 1 - ε + ε2. Compute α1 and α3 with this approximation.
The additional term a2(VGS - VTH)2 is multiplied by K(VGS - VTH)2, yielding two terms of interest: 4Ka2Vin(VGS - VTH)3 and 4Ka2Vin3(VGS - VTH). The former contributes to α1 and the latter to α3. It follows that
Solution: